## Slide 1: ABM and Cities
Alex D Singleton, Seth E Spielman, David C Folch (2017) Urban Analytics. London: Sage.

## Slide 2: Learning Objectives
Differences between aggregate and disaggregate modeling frameworks.
The main features of cellular automata, microsimulation, and agent-based modeling.
What agents are, and how they function within an agent-based model.
Those features of a complex system.
Constraints on the operational use of agent-based models.

## Slide 3: Cities as Interacting Parts
Possible to consider cities as collections of interacting entities.
When cities are studied at an aggregate level it is often difficult to observe outcomes that may emerge through a collective of individual-level behaviors
Popularity of aggregate modeling
  Historically limited availability of disaggregate data
  Often easier to implement aggregate modeling
  For applications that require empirical specification or evaluation, urban data are more prevalently available at an aggregated rather than individual scale

## Slide 4: Cities as Interacting Parts
Problems with aggregate models
  Can be constraining when an objective of the analysis relates to the examination of individual behaviors
    Specifically when these are concerned with interactivity or non-linear dynamics
Three of the main methodological frameworks
  Cellular automata
  Spatial microsimulation
  Agent-based modeling.

## Slide 5: Schelling Model
Thomas Schelling – US Economist (1921 – 2016)
The motivations of individuals can create aggregate level outcomes that are at odds with what individuals want
  E.g - If individuals prefer to live in a neighborhood that is 51% the same race
    a fairly integrated neighborhood
  The cumulative results of individuals seeking such a neighborhood composition is that almost total segregation emerges.
    The individual motives (for integration) would not have been observable from the aggregate (segregated) landscape.
Schelling first developed this idea as simple checkers like game, but it was subsequently converted into computer models

## Slide 6: Schelling Model
A NetLogo implementation of the Schelling model
Source: Wilensky, U. (1999). NetLogo. http://ccl.northwestern.edu/netlogo/. Center for Connected Learning and Computer-Based Modeling, Northwestern University, Evanston, IL.

## Slide 7: Cellular automata
Defined as a grid of cells (like a checker board), each cell is called an “automata”.
Each automata stores a numeric value.
As a model runs through a series of time steps, each automata can change their assigned value (state) based on a set of rules which takes into consideration those values in the surrounding cells (neighborhood).
A SLEUTH model for San Diego in 2030 showing predicted levels of urbanization Source: Keith Clarke, UCSB, USA. Reprinted with permission.

## Slide 8: Agent Based Models
Agent-based modeling (ABM) is a collective term for a software simulation technique that enables interactivity between individual entities
Some popular open source ABM frameworks

## Slide 9: Agent Based Models
Typically initiated with a simple set of rules that are specified at a micro level (e.g., individuals)
  derived from theory / empirical observation
Rule sets govern how each agent interacts with the other agents within the simulation and their environment.
Over the course of a simulation the macro-level outcomes emerge as a result of a complex of individual-level adaptive behavior, including various types of non-linear dynamics
  referred to as emergence

## Slide 10
Desire paths as an example of an emergent feature Source: Photograph by George Redgrave CC BY-ND 2.0 (Flickr).

## Slide 11: Complex Systems
Multiple equilibrium
  Models may have a number of steady states that are maintained under quite different parameter settings.
Non-stationary
  Stochastic outputs that change after each run.
Self-organization
  Various dynamic behaviors ranging from chaotic to regular oscillations between different steady states.
Phase transitions
  May occur between different steady states.

## Slide 12: Agent Based Models: Example
A MASON graphical user interface showing a cholera disease agent-based model of the Dadaab refugee camp in Kenya. Source: Crooks and Hailegiorgis (2014). Reproduced with permission.

## Slide 13: Agent Based Models: Example
Graphical output showing different traffic volumes Source: www.matsim.org/scenario/quito-ecuador. Reproduced with permission.

## Slide 14: Agent Based Models: Example
An agent-based model considering burglary Source: Malleson (2010). Reprinted with permission.

## Slide 15: Conclusion
Disaggregate modeling has a particular use case over aggregate models
  Useful for the exploration of complex systems
Various modeling frameworks / approaches; multiple software implementations